ROOF REPLACEMENT

MACKENZIE HALL

110 SHERMAN STREET

HARTFORD, CONNECTICUT

BI-2B-355

| Original Bid Due Date / Time: | 2/13/13 | 1:00 pm |
| --- | --- | --- |

| Revised Bid Due Date / Time: | 3/6/13 | 1:00 pm |
| --- | --- | --- |

| Previous Addendums: | 1,2 & 3 |
| --- | --- |

TO: 	Prospective Bid Proposers:

This Addendum forms part of the “Contract Documents” and modifies or clarifies the original “Contract Documents” for this Project. Prospective Bid Proposers shall acknowledge receipt of the total number the Addenda issued for this Project on the space provided on Section 00 41 00 Bid Proposal Form.  Failure to do may subject Bid Proposers to disqualification.

The following clarifications are applicable to drawings and specifications for the project referenced above.

Item 1

DRAWING 1/A-1 –

SITE PLAN:	REVISED:  See attached Site Plan drawing for change in Contract Limit Line location and additional indication of flood prone area.

### Item 2

DRAWING 1 and 2/A-2 –

ROOF PLANS:	Where stated, “Remove & replace sealant / mortar in reglets & coping joints”.   CHANGE to:	 “Remove sealant / mortar in reglets & coping joints and                install new sealant”.

ADD: 		 Include above sealant work in reglets & coping joints around Roof N (on tower).

### Item 3

DRAWING 1/A-4 –

REBUILDING FALSE

CHIMNEY #2:			The text - “New handmade bricks”.

CHANGE to:	“New bricks”.

Item 4

04 01 20

MASONRY RESTORATION – 	DELETE:  04 01 20.2.1.A.2 – “For special shape bricks…”.  Modular face brick will be used as noted in 04 01 20.2.1.A.1.

END OF ADDENDUM NUMBER 04 (FOUR)

David Busanet, Bidding & Contracts Supervisor

Department of Administrative Services

On Behalf of the Department of Construction Services